## Slide 1
Delivering Digital
Services
Aeronautical
Data
in Airline Operations
Presented By: Reinhard Thanhäuser
Lufthansa Systems
Date: August 26, 2014

## Slide 2
1
Flight Planning
Charting
Network Planning
FMS
Aircraft Perf
Load Control
OPS Control
Crew Planning
Check-In
Sales Ticketing
Airline IT

## Slide 3
Flight Planning
Strategic Planning
Operational Planning
Tactical Planning
Inflight Support
Postflight Analysis
2
Long Term
Short Term
Actual Flight Event
During Flight
After Flight
Route
Evaluation
Network
Planning
Overflight
Clearance
Performance
Data
Route
Optimization
Fuel
Optimization
Operational
Flight Plan
Latest
Changes
NOTAM
Watch
Weather
Watch
Statistics
Fuel Policy
Baseline Data
Statistics
Baseline Data
Baseline Data
Temporal Data
Baseline Data
Temporal Data
Fuel Consumption
Flight Time

## Slide 4
Operational Planning
Goals
Legal flight plan
Safe flight
Economic flight
Pilot (End User) Support
Briefing package
  Routing
  Fuel calculation
  Weather
  Restrictions
  NOTAM
Consistent information
  Operational flight plan
  FMS
  Charting
Inflight support
3

## Slide 5
Temporality
Tailoring
Required Data
Navigation Data
Weather Data
Operational Data
5

## Slide 6
Navigation Data
Common Data
Static data
NOTAM
Restrictions
Rules
Regulations
Tailored Data
Customers ask for data tailoring
Different view on the world
Operational reasons
  Operational risk
  Equipment
Political reasons
  Local agreements
  Flight restrictions
6

## Slide 7
Operational Data
Flight Event Data
Aircraft rotation
Crew rotation
Booking data
ATS flight plan
Aircraft performance
Aircraft equipment
Customer Policies
Fuel policy
Special procedures
Airport authorization
Traffic rights
Crew qualification
Statistics
Cost index
7

## Slide 8
Weather Data
Airport Weather
METAR
TAF
Runway conditions
Evaluated for
  Departure
  Destination
  Alternates
  ETOPS alternates
Enroute Weather
Upper Air Data
Significant weather charts
Other weather phenomena
8

## Slide 9
Other Data
Flight Planning
Cosmic radiation
Environmental data
Special flight planning data
  Life vest airspace
  Directs
  Artificial waypoints
  Non-published data
Fuel price
Admin
System configuration
User rights
Dispatch offices
9

## Slide 10
Temporality
Validity
Lifecycle
Time schedules
Changes during lifecycle
Short term changes (NOTAM)
No overlaps in temporality
Flight Planning Impact
Flights „between“ AIRAC cycles
Complex evaluation
  Determination of current state
  Manual evaluation of NOTAM may be required
Data integrity
10

## Slide 11
Data Tailoring
0 7
2 5
3900 m
700 m
AIRAC
AIRAC
AIRAC
AIRAC
AIP
Data Provider
Mega - Air
Micro - Air
9300 m
3900 m
3200 m (FPL)
3900 m (FMS)
3900 m (FPL)
3900 m (FMS)
3900 m
9300 m
1000 m
4000 m
3900 m
4000 m
3900 m
3200 m (FPL)
4000 m
3900 m (FMS)
4000 m
4000 m
3900 m (FPL)
4000 m
3900 m (FMS)
4000 m
NOTAM
2900 m
11

## Slide 12
Data Sources
Navigation Data
AIP
Amendments
Supplements
Circulars
NOTAM
Military publications (if available)
ATC
Customer Data
Customer policies
Customer manuals
Contracts
Communication
Other Sources
Topography/Terrain
Charts/Satellite images
Independent organizations
Weather Data
Weather providers
12

## Slide 13
Data Maintenance
Lido/Flight
24/7 data provider
Worldwide coverage
Quality assurance
More than 2500 documents per year
Increasing amount of data
Manual editing process
Huge manpower
Application related
Partly automated NOTAM parser
Automated WX import
Mostly automated OPS data import
13
Chart: Lido/Flight NOTAM Processing

## Slide 14
Data Structures
16

## Slide 15
Life is not always easy …
Data Quality
Inconsistent data
Incomplete data
Untrusted data
Ambiguous data
Briefing
Different processing time
  Flight planning
  Charting
  FMS
Different data providers
Flight Planning
Insufficient data
Unspecified NOTAM
Handling of complexity
17

## Slide 16
Example
6 NM
Inconsistent Data
Three definitions of the same waypoint
Two countries
18

## Slide 17
Example
O0186/14 NOTAMN
Q) ****/QFAXX/IV/NBO/A/000/999/4146N****E****
**** B) 1408180700 C) 1410180400
E) RWY 09L: METAL FENCE HGT 2M INSTL AT DIST 160M FM RWY EXTREMITY
TOWARDS LMM. RWY SHOULDER AND STOPWAY REDUSED BY 240M.
STRIP DIMENSIONS: 3260 X 202M.
CREATED: 18 Aug 2014 07:13:00
662 R
LMM
662 V
LMM
Ambiguous Data
There is no stopway .
Which LMM ?
RWY | TORA | TODA | ASDA | LDA
09L | 2600 | 3000 | 2600 | 2700
27R | 2600 | 3000 | 2600 | 2700
19

## Slide 18
Example
Complexity
How does a bulb affect flight operations ? A case study…
Airport Suitability Check
Lido/Flight checks destination and all possible alternates for suitability
  At the ETA
  Weather forecast
  Weather minima
  Fire fighting category
  NOTAM situation
  …
A Broken Light Bulb
May downgrade the approach lights
May close and approach procedure
May close the airport
May force the aircraft to divert
May cause a delay
May cause that the crew exceeds allowed duty times
May cause an additional night for the passengers
…
20

## Slide 19
Requirements
Advantages of digital data
Automated processing
Unique data
Timely availability
Ready for visualization
Digital data shall be
Compliant with standards
  ISO
  ICAO/IATA
  DO 200
Quality assured
  Business rules
  ADQ
Unique and identifiable
Consistent
Complete
  Static data (Baselines)
  Temporal data (Delta)
Extendable
Reliable
21

## Slide 20
Paper versus AIXM
ANSP Survey (2011)
Survey was contacted by Lufthansa Systems FlightNav
85 of 169 organizations answered the survey
  How is aeronautical data published today?
  How will aeronautical data be published in the future?
Today
AIXM Usage
22

## Slide 21
Vision
If I could make a wish …
XMs would become a common „language“ between all airspace users
XMs would be fully implemented in SESAR and NextGen
ANSP world would be merged with the airline world
ANSPs would provide a one stop shop for aeronautical data
Flight planning systems would be able to connect to different data providers
The entire AIP would be available in AIXM
Data would be available without delay
Data would be quality assured and always consistent
Data changes would be applied directly to the database
23

## Slide 22
Conclusion
AIXM
AIXM is a mature data model ready for use
Data content is still only available marginally
Please provide not only NOTAM, but also static data
Quality assurance has to be implemented
XMs
are the right way to answer our challenges
are more than an interface
can be fully utilized, if the philosophy behind is consequently implemented
Should be further enhanced in close cooperation with airspace users
Thank you !
24

## Slide 23
Contact Information
Reinhard Thanhaeuser
Performance and Operations Engineering
Lufthansa Systems AG
FRA AF/L-SP
Am Prime Parc 2
D-65479 Raunheim
Germany
Tel.: +49 69 696 90922
E-mail: Reinhard.Thanhaeuser@lhsystems.com
25